## Slide 1
BADGE FINDER
Finding a friend with borrowed WiFi
Hack the North 2026 · custom ESP32-C3 badge firmware

## Slide 2
THE SCENARIO
You're trying to find your friend
at Hack the North.
your friend is in here. somewhere.
1,000+
hackers in one building
0 bars
of cell signal in the hall
“by the tables”
describes every corner of the venue
Your badge can help — if we replace its firmware.

## Slide 3
THE HARDWARE
The badge in your hands
WHAT IT HAS
WiFi — full scan, ESP-NOW, SoftAP
802.11mc FTM — time-of-flight ranging
BLE — raw advertise + scan
Accelerometer — step counting
6 RGB LEDs + 320×240 display
WHAT IT DOESN'T
GPS — useless indoors anyway
Magnetometer — no compass
Gyroscope — can't track turning
UWB / AoA antennas — no AirTag tricks
The badge has no idea which way it is pointing. Everything that follows is about earning a direction anyway.

## Slide 4
WHAT WE CAN MEASURE
A distance is only a ring
A (you)
|AB| = 5.0 m
802.11mc FTM measures round-trip time of a WiFi frame — distance to the other badge, accurate to a metre or two.
But with no compass and no gyro, that number is only a radius. Your friend could be anywhere on the ring.
What we need is a direction to walk.

## Slide 5
THE KEY INSIGHT
We are not alone in the room
AP1
AP2
AP3
A
B
5–8 access points are visible from anywhere in the venue
They never move
Both badges can see the same ones
Free, static reference points — shared by both badges.

## Slide 6
HOW THE MATH WORKS
two captures, one short walk

## Slide 7
STAGE 1 · FIRST CAPTURE
Choose a frame
A = (0, 0)
B = (d, 0)
d = 5.0 m from FTM
We know the distance d between the badges — but not the bearing. So we build the only frame we can: A at the origin, B on the x-axis, by construction.
B scans the same APs and sends its list back over ESP-NOW. 8 APs × (6 B BSSID + 1 B RSSI) = 56 bytes — one packet.

## Slide 8
STAGE 1 · FIRST CAPTURE
Two circles, two answers
P₁
P₂ (mirror)
For each shared AP:
x = (d² + dA² − dB²) / 2d
y = ±√(dA² − x²)
RSSI path loss gives rough distances dA and dB to the AP. Circle about A, circle about B — they cross at two points, mirror images across AB.

## Slide 9
STAGE 1 · GEOMETRY CHECK
All the chords are parallel
every chord ⊥ AB
Team hypothesis, verified: the two candidates of every AP are reflections across AB, so every chord is exactly perpendicular to AB — all of them parallel. Checked numerically: 90.00°, every time.
The catch: we chose the frame that put AB on the x-axis. In the only frame we can build, “perpendicular to AB” is true by construction — it recovers the axis we picked, not a real-world direction.

## Slide 10
STAGE 1 · THE LIMIT
We know the axis — not the direction
A
B?
or B?
The chord midpoints pin the axis A should move along — the A–B line is known. But both directions along it fit the data equally well: toward B, or exactly away from it.
Stage 1 alone cannot tell you which of the two ways to walk.

## Slide 11
STAGE 2 · SECOND CAPTURE
Walk a few steps, measure again
A₁
A₂
B
×
×
×
Steps count the displacement — ≈0.72 m each
Direction is “straight ahead” in your own body frame — a direction you can feel
Re-scan from A₂: only one candidate in each mirror pair fits the new distances
Three anchors — A₁, B, A₂ — kill the reflection and pin the map to your walk
θ = arccos(−Δd / Δwalked) keeps the compass live while you walk

## Slide 12
HONEST NUMBERS
Why this beats spinning in place
±29° → ±15–25°
expected bearing error, vs a single body-shadow spin
1 → 5–8
constraints per capture — over-determined, robust to any one bad AP
56 bytes
of data exchanged — one ESP-NOW packet
Multipath errors on different APs are largely independent — they average out. RSSI→distance is still the weak link (factor-of-two typical): the rings are thick annuli, not thin circles.
And the endgame: APs are static. Solve their positions once, cache the map — every later locate is a single scan. No walking, no spinning.

## Slide 13
ERRORS & ASSUMPTIONS
What can go wrong
THE ERROR
30–50%
typical error in a single WiFi distance estimate — signals bounce off walls, fade, and interfere.
The fix: a rolling average. Each scan is noisy, but the noise is different every time — averaging successive scans smooths the jitter into a stable estimate.
THE ASSUMPTIONS
No bodies in the way — a person between the badges soaks up 10–20 dB and reads as extra distance
Not too much obstruction between them — walls and dense crowd stretch every apparent range
This is a hallway-scale finder, not an AirTag — and it says so honestly
When the assumptions break, the arrow drifts — the rolling average keeps it from lying confidently.

## Slide 14
DEMO
live, on two badges

## Slide 15
Questions?
Hack the North 2026 badge · custom ESP-IDF firmware · ±17° with three spins averaged